## Slide 1: PACE Proper Analysis of Coherent Excitations
HORACE
Package for analysing results of inelastic experiments
https://pace-neutrons.github.io/Horace

## Slide 2
MERLIN PSD Detectors
Inelastic experiment using direct inelastic instrument.
Measure

## Slide 3
  70,000 detector elements
  300-500 energy bins
  Upto 4 or 5 different Ei simultaneously
MERLIN spectrometer (ISIS)
Measuring Excitations

## Slide 4
MERLIN PSD Detectors
Inelastic experiment using direct inelastic instrument.
Measure

## Slide 5
MERLIN PSD Detectors
Inelastic experiment using direct inelastic instrument.
Measure

## Slide 6
A surface in 4-Dimencional q-dE space
Inelastic experiment using direct inelastic instrument.
Measure

## Slide 7
Inelastic experiment using direct inelastic instrument.
Single crystal position provides hypersurface in 4-D space. To cover whole 4-D volume, use rotating crystal. Typical experiment – 200 runs

## Slide 8
Indirect inelastic instrument:
MUSHRUM will change the game

## Slide 9
From experiment to scientific result: HORACE-PACE workflow
Convert Time of flight to energy transfer
View, enhance and analyse
Construct 4-D
Compare with scientific models
Scientific models
MANTID
HORACE sqw object
HORACE
Tobyfit
SpinW – linear spin wave theory
Euphonics – results of DFT calculations
User models
MANTID MD workspace
MANTID fitting
Instrument models?

## Slide 10
HORACE structure:
SQW object (Filebacked)
1-4D image in reciprocal coordinate system
Experiment info
Pixels (All neutron events)
Multifit
Fitting engine
Tobyfit
Instrument info
ISIS instruments models
Resolution function & Resolution convolution
Algorithms to operate with sqw object
CUT
plot
Image is calculated as average from pixels
and serves as the “key” for pixel database

## Slide 11
HORACE Workflow:
https://pace-neutrons.github.io/Horace
https://isis.analysis.stfc.ac.uk/workspaces
MARI, MERLIN, MAPS, LET
excitations-single crystal machine
There is a GUI (horace)
/mnt/ceph/auxiliary/excitations/rse_training