Machines performance on gen_sqw and combine (30Gb)
ndmlnx01
n-workers
cache-size
iDaaaS large
n-workers
cache-size
iDaaaS Small
lnxT7500

---
Testing on 21/04/202. iDaaaS large. Broken:
Time to combine 30Gb sqw file
from 50 tmp files.
Time to generate 30Gb sqw file
from 50 nxspe files
N parallel workers
Combine buffer size(bytes)
Testing on 01/05/2020. iDaaaS large (fixed)
Time to generate 30Gb sqw file
from 50 nxspe files
Time to combine 30Gb sqw file
from 50 tmp files.
Time to combine 150Gb sqw file
from 250 tmp files.
Time to generate 150Gb sqw file
from 250 nxspe files
Time (sec)
Time (sec)

---
04/05/2020 Persistence. iDaaaS large. Two runs 150Gb
05/05/2020 Isiscompute. 150Gb

---
01/07/2020 iDaaaS large vs isiscompute. New FS update. 32Gb (50 contribution nxspe)
n-workers
cache-size
Old isiscompute (see slides above)
Testing on 06/07/2020. iDaaaS large (New FS)
Time to generate 30Gb sqw file
from 50 nxspe files
Time to combine 30Gb sqw file
from 50 tmp files.
n-workers
cache-size
Old idaaas (see slides above)
n-workers
cache-size

---
06/07/2020 iDaaaS large vs isiscompute. New FS update. 150Gb (250 contribution nxspe)
Old isiscompute (see slides above)
Old idaaas (see slides above)
New one has 2 times faster disc access speed

---
27/07/2021 iDaaaS. Parallel vs serial performance. 122Gb RAM, 30CPU core node + Slurm cluster: 32 of 16Gb nodes

---
Local parallel vs Remote parallel performance (27/07/2021)
Speed deteriorates substantially for “Remote” files. The further files are, the worth is the performance
tser = tw+tr+tc~tIO+tc~2*tChar-- Serial task timing
serial task (28min)
Max IO processing speed ~1Gb/s (sometimes achieved when combined locally with smaller sqw files)
Slurm parallel 25% faster local parallel if configured
properly. If not, 10-times slower
TODO:
1) Try prefetch
2) Try fully parallel task
     (prefetch will still be desirable)
25% random variations in the processing (IO) speed

---
Reference results from very old machine
(Ubuntu T7500)
Combine speed as function of buffer suze. Point x=0 – Mode 0, 1-read-all/1- write thread.

---
Profiling
“Local” files
“Remote” files
Quick for “local” slow for “remote” files routine